## Slide 1: Factorial Design
ChemE 436
Chad Curtis
Autumn 2019
Notes: Introduction to course: purpose.
  Introduction to Slack
Poll Everywhere survey
Go through syllabus

## Slide 2: Lecture objectives
Perform statistical analysis to quantify uncertainty in calculated quantities.
Calculate uncertainty using both error propagation and bootstrapping methods.
Present data in both tabular and graphical form.
Notes: Translate customer needs into a testable hypothesis and experiment.

## Slide 3: Example 1
Goal: determine how 4 factors (temperature, concentration, catalyst, other) affect reaction yield and which are important.
Full 24 factorial with each point replicated. Total 16 runs.

## Slide 4: Factorial Experimental Design
Well suited for exploration: What is important?
Provide maximum information for effort expended.
Vocabulary:
  Factor: An independent variable (e.g. temperature, pressure, concentration). Must be at least 2.
  Response: The dependent variable (e.g., yield)
  Level: A factor’s value (e.g. 100°C). Can be qualitative (e.g., on/off)
  Main Effect: The response to a particular factor with other factors held constant.
  Interaction: The response to a simultaneous change in 2 or more factors.

## Slide 5: Factorial model
Assume a model of form:
Model is non-linear.
Main effects
2-way interaction
3-way interaction
4-way interaction

## Slide 6: Choosing factor levels
Focus on quantitative factors for now.
Choose range for each factor
  Large enough to cause measurable response (if one exists)
  Consider normal “move size”
  Not so large that response “saturates”
  May require some try and error
Choose pi, number of levels for ith factor
  Require pi > 1
  Define levels by dividing range into pi - 1 equal increments
  If pi = 2, levels are lower and upper ends of range

## Slide 7: Coding factor levels
Conventional to code (scale) the levels for each factor.
  Let zi be the coded version of factor xi .
  Suppose xi,min and xi,max are the minimum and maximum level for this factor.
  Then, by convention, define
(pi values)
  Remark:
    zi varies between -1 and +1 as xi varies between xi,min and xi,max.
    zi = -1 or +1 for two levels

## Slide 8: Visualization factorial experiments
Coded experiments (levels to be tested) are vertices of a square (p =2, n = 2), or a cube (p = 2, n = 3) centered on the origin.
For p = 2, n > 3, it’s a hypercube (hard to visualize ...)
z1
z2
(+1,+1)
(+1,1)
(1,1)
(1,+1)
P = 2, n = 2 ( 22 = 4)
z2
z3
z1
(1,+1,+1)
(1,1,+1)
(1,+1,1)
(+1,+1,1)
(+1,1,1)
(+1,+1,+1)
(+1,1,+1)
(1,1,1)
P = 2, n = 3 (23 = 8)
Go to example 

## Slide 9: Orthogonal vectors
Two vectors are orthogonal when they are mutually perpendicular.
The projection of one vector onto the other has zero length.
A
B
No projections --
Vectors A and B are orthogonal.
Inner product
If the inner (“dot” or “scalar”) product of two vectors is zero, the vectors are orthogonal.
To compute the inner product, multiply corresponding elements and sum.
A | B
1 | 1
-1 | 2
Inner product of these two vectors is:
So they are not orthogonal
A (1, -1)
B (1, 2)

## Slide 10: What’s under the hood
Suppose X and y contain the data:
  - X is a matrix with N rows and n columns, where
    N = number of experiments
    n = number of independent variables
  - y is a column vector with N rows.
b is a column vector of constants to be estimated, n rows.
X11 … X1n y11 b11
. . .
. . . bn1
. . .
XN1 … XNn yN1

## Slide 11: Matrix form
=
*
y = X * b
Added column to X matrix to account for the b0 term
n
N

## Slide 12: Least-squares Regression
The least-squares estimate of b involves the following matrix operations:
Multiply both sides by X transpose
X TX is n by n. IF it is invertible,
*
=
XT
y
XTy
XTy is inner product of y with each column of X
(or each row of XT).
N
n

## Slide 13: LSR: Test Case
XTX
*
=
XT
X
XT X
= 16 I
where I is the identity matrix, n by n.
Go to example 

## Slide 14: Uncertainty analysis
If y includes random effect, N(0, y), its propagation to b is:
Thus:
All b elements have the same uncertainty
There is no cross-correlation between elements of b
The standard deviation for each b element is 2.83/4 = 0.707
For the full factorial design with orthogonal X, this reduces to
cov(b): covariance
cov(b) = σ(b, b) = σb2

## Slide 15: What is a full factorial is too much work?
Using first 8 runs of Expt. 1 only.
8 parameters, so model fits data exactly.
“Overparameterized” model – bad practice.

## Slide 16: Motivation for partial factorials
As n increases, full factorial requires many experiments.
A response surface for two factors
Fewer levels may miss the conditions
for the optimal responses
Also might want to use p > 2 (to test for “curvature”).
  Example: pi = 3, zi = -1, 0, +1 for all n = 3 variables
  Full factorial requires 33 = 27 experiments + replicates.
Interactions often small, especially 3-way and greater.
  Omitting them from model allows fewer experiments
Alternative: Partial factorial design.

## Slide 17: Partial factorial design
If we assume that there are no interactions, simpler model requires fewer experiments.
  Example: n = 3 requires 4 parameters:
  Requires at least 4 experiments.
  Use the best 4 experiments.
Best: “unconnected” vertices
(1,+1,+1)
(1,1,+1)
(1,+1,1)
(+1,+1,1)
(+1,1,1)
(+1,+1,+1)
(+1,1,+1)
(1,1,1)
Either the orange or black
combinations would be good.

## Slide 18: Partial factorial design
A poor choice
(1,+1,+1)
(1,1,+1)
(1,+1,1)
(+1,+1,1)
(+1,1,1)
(+1,+1,+1)
(+1,1,+1)
(1,1,1)
Poor coverage.
Three of the four points have
z1 = -1 and z3 = +1.
A terrible choice
(1,+1,+1)
(1,1,+1)
(1,+1,1)
(+1,+1,1)
(+1,1,1)
(+1,+1,+1)
(+1,1,+1)
(1,1,1)
If points are on one face, an independent variable is being held constant. Can’t invert XTX.
Go to example 

## Slide 19: Handling qualitative variables
Example 1 included a qualitative variable (catalyst type).
  We coded one type as +1, and the other as -1.
What if there had been 3 (or more) catalysts?
  Coding the three as one variable with levels +1, 0, -1 would lead to incorrect conclusions.
  Implies catalysts are “ordered,” but they are discrete and independent.

## Slide 20: Handling qualitative variables
Replace each qualitative variable having p > 2 levels with p-1 new variables, each having two levels (0 and +1).
Example 1: catalysts A, B, and C
  p = 3, so define 2 variables:
    x1 = +1 if type A, otherwise 0.
    x2 = +1 if type B, otherwise 0.
  Thus, only 3 combinations of x1 and x2 are possible.
    If catalyst = A, x1 = +1, x2 = 0
    If catalyst = B, x1 = 0, x2 = +1
    If catalyst = C, x1 = 0, x2 = 0

## Slide 21: Handling qualitative variables
Example 2: catalysts A, B, C, D
  Replace with 3 variables:
    If catalyst = A, x1 = +1, x2 = 0, x3 = 0
    If catalyst = B, x1 = 0, x2 = +1, x3 = 0
    If catalyst = C, x1 = 0, x2 = 0, x3 = +1
    If catalyst = D, x1 = 0, x2 = 0, x3 = 0
Pattern: one (and only one) of the new variables is “on” (level = +1) or all are “off”.